## Slide 1
TETHER SATELLITE SYSTEM DYNAMICS MODELLING
Chen Kaiwen
co-worked with Dr. Pok Wang KWAN
Supervised by Prof Xun Huang
Master of Science in Aeronautical Engineering
Department of Mechanical and Aerospace Engineering
School of Engineering HKUST
May. 2018

## Slide 2: Outline
Motivation
Literature Review and Case Study
Detection using ArduSat Demosat
Wireless communication Setup
Testbed fabricating
Acknowledgement

## Slide 3: Motivation
The Earth is surrounded by tens of thousands of sizeable chunks of debris orbiting at very high speeds
Add to these larger pieces debris an estimated hundreds of thousands of sub-centimeter-sized artificial particles
A source for potential disaster—for while these small particles may not seem imposing, they can present a serious threat to functional spacecraft.
Tracked space debris in 1963 and fifty years later in 2013.
Image credit: NASA

## Slide 4: Motivation
Debris Kind:
  Fragmentation Debris
  Spacecraft
  Mission-related Debris
  Rocket Bodies
  Other sources
Debris changing trend over nearly 60 years
——From 1957 to 2013
“Since 2002 ,The growth(of space debris) has entered into the more feared exponential trend.”
——Donald Kessler: former NASA scientist

## Slide 5: Motivation
Actively Removing Space Debris
Artist's rendition of the JAXA space debris collection mission. Credit: JAXA
ESA's e.Deorbit space debris collection mission. Credit: ESA
A space debris removal satellite, dubbed Sling-Sat, designed at Texas A&M University.

## Slide 6: Literature Review
Hovell, K., & Ulrich, S. (2017). Experimental Validation for Tethered Capture of Spinning Space Debris. In AIAA Guidance, Navigation, and Control Conference (p. 1049).
Operating state:3-degree freedom of motion, X Y and rotation
New configuration idea: Sub-tether configuration
Key physical quantities: Target tether angle ; Target angular rate; Total angular momentum
Goal: Decrease all the key physical quantities much quicker to make space debris deorbit practically

## Slide 7: Literature Review
Assumption
Massless tether; constant end-body mass, visco-elastic tether
3 Degree of Freedom, Planar Dynamics, for chaser and target
  Translational motion along X axis and Y axis,
  Rotational motion about the Z axis,
No external forces applied to the center of mass of the whole tethered satellite system
The Inertia matrix is constant and the body frame of each of the end-masses is aligned with the principal axes of the end-masses

## Slide 8: Literature Review
Reference frame andCoordinate system
  Defined as right-handed system
  Inertial reference frame FI
    Reference inertial frame FI Coordinates = [Ix , Iy , Iz]
    Fixed, position of origin point and direction of x , y , z axis don’t change with time
  Target body-fixed frame FT
    Reference inertial frame FT Coordinates = [Tx , Ty , Tz]
    Origin point at the center of mass of the target
    The x axis of target is pointed to the chaser at the beginning
  Chaser body-fixed frame FC
    Reference inertial frame FC Coordinates = [Cx , Cy , Cz]
    Origin point at the center of mass of the chaser
    The x axis of chaser is pointed to the chaser at the beginning

## Slide 9: Literature Review
  Coordinate transformation
    Attitude matrix : transformation matrix that rotate the vector components from a body frame to Inertial frame
    attitude of a body frame is the angle of rotation between the body frame relative to the Inertial frame FI about the z-axis where the z-axis of all inertial and body frames are parallel
    Vectors from Body frame to Inertial frame
: Tether attachment vector with respect to the body center of mass, which is fixed in the body frame

## Slide 10: Literature Review
Tether length
Tether tension
Governing equation: Newton’s second law and Euler’s equation
Since reference inertial frame is not rotating around the inertial frame
  Torque with respect to the inertial frame equals torque with respect to body frame
  Angular velocity of an end-mass relative to the inertial frame also equals to the angular velocity relative the body frame
Physics Model for the system
  Nonlinear stiffness, spring damper system
  The damping coefficient of the damper is constant
  Nonlinear spring constant, tether materials : 56% polyester and 44% rubber
    The spring constant changes as the extension of tether change
    When tether is extended, the spring force
    =0 when tether is slacked

## Slide 11: Literature Review
Tether Length
Tether tension
  Damping force: , damping factor multiply the velocity change in the tether’s direction
  :Unit vector of tether

## Slide 12: Literature Review
Tether torque
  the moving frame’s absolute angular velocity, doesn’t exist in this case(=0)
    The moving frame just has translational motion in Inertia frame
  =0
  ==
    Torque in inertial frame = Torque in body frame
Euler’s equation
  =
  =
    =

## Slide 13: Case study
Hovell and Ulrich (2017) planar single tether thrust stabilization
- Tether angle simulation t = 1-100 s
Kirk Hovell
Kaiwen Chen

## Slide 14: Case study
- Target vehicle angular velocity t = 1-100 s
Kaiwen Chen
Kirk Hovell

## Slide 15: Detection using ArduSat
Arduino Cubusatellite Standard 1U Demosatellite
-Sensor board’ sensors
Accelerometer
Gyroscope
Magnetometer
Compile the Arduino Board using Arduino ino file
CSV format: include timestamp
Highest baud rate 57600 for improving motion-tracking effect
Individual written MATLAB code for real-time data plotting and recording via USB serial communication
Figure: Ardusat Demosat

## Slide 16: Detection using ArduSat
Update rate: 32HZ
Acceleration: Sensor LSM303 triple-axis accelerometer
Angular rates: Sensor L3GD20 three-axis gyroscope.
Orientation: derived from acceleration
and Magnetic intensity

## Slide 17: Wireless communication Setup
Xbee on Ardusat A(Target)
Xbee on A Shield
Xbee on B Shield
Xbee on Ardusat B(Chaser)
B network
A network
The two network should be separated. The wireless network transmission should not be interfered by the other network.
Figure: Illustration of one network

## Slide 18: Wireless communication Setup
Table: Xbee Part setting
Key point: Each following one way and against the other at the same time respectively
Xbee on Ardusat A(Target)
Xbee on A Shield
Xbee on B Shield
Xbee on Ardusat B(Chaser)
B network
A network
Archived lowest interference setting

## Slide 19: Testbed fabricating
Original model

## Slide 20: Testbed fabricating
SolidWorks Motion Analysis
Mass of Inertia along two axes are different
Using constant force along two axes
Blue line and red line shows the linear acceleration of two directions. The magnitude of them are totally different.

## Slide 21: Testbed fabricating
Compensation configuration
  Using two pairs of simulator and physical connection
Hanging configuration
  Using string to provide additional rotational degree of freedom

## Slide 22: Acknowledgement
I would like to express my special thanks of gratitude to my supervisor Prof Xun Huang ,who gave me the opportunity to do this wonderful project on the topic Tether Satellite System and generous help, as well as to my mentor Dr. Pok Wang KWAN, who devoted his time caring and helped me to manage my project.
By doing a lot of research training with him I came to know about so many new things and practiced a lot of useful skills such as MATLAB Programming, Arduino, Latex Report writing and XCTU wireless communication.
The most valuable things I learned are the self-learning skill, problem-solving logical thinking and markdown custom. I am really thankful to them.
Secondly I would also like to thank my friends and PhD colleagues who helped me a lot in finalizing this project within the limited time frame.
Thank you for listening